## Slide 1
UNIT 3

## Slide 2
Unit-3 Teaching Hours: 10
Data link Layer
Chapter 10 Error detection and correction: Introduction – Checksum.
Chapter 12 Multiple Access: Random access (ALOHA, CSMA, CSMA/CD and CSMA/CA.)– Controlled Access: Reservation – Polling – Token Passing. Channelization: FDMA - TDMA.
Chapter 14 Wireless Lans: IEEE 802.11 - Architecture – MAC sub layer - Addressing Mechanism – Physical layer - BLUETOOTH : Architecture – Bluetooth layers.
Chapter 15 Connecting LANs, Backbone Networks, and Virtual LANs: CONNECTING DEVICES – Hubs – Repeaters – Bridges – Switches – Routers – Gateway.

## Slide 3
Unit-3
Data link Layer
Error correction and detection: Introduction – checksum Multiple Access: Random access – Aloha – Controlled Access: reservation – polling – token passing. Channelization: FDMA - TDMA Wireless Lans IEEE 802.11 - architecture – MAC sub layer Addressing mechanism – physical layer - Bluetooth: architecture – Bluetooth layers. Connecting Devices – hubs – repeaters – bridges – switches – routers – gateway.

## Slide 4
Chapter 10
Error Detection and Correction

## Slide 5
Error correction and detection
        Introduction
        Block coding
        Checksum

## Slide 6
Data can be corrupted during transmission.
Some applications require that errors be detected and corrected.
Note

## Slide 7
10-1 INTRODUCTION
Let us first discuss some issues related, directly or indirectly, to error detection and correction.
Types of Errors Redundancy Detection Versus Correction Forward Error Correction Versus Retransmission Coding
Modular Arithmetic

## Slide 8
In a single-bit error, only 1 bit in the data unit has changed.
Note

## Slide 9
Single-bit error

## Slide 10
A burst error means that 2 or more bits in the data unit have changed.
Note

## Slide 11
Burst error of length 8

## Slide 12
To detect or correct errors, we need to send extra (redundant) bits with data.
Note

## Slide 13
The structure of encoder and decoder

## Slide 14
10-2 BLOCK CODING
In block coding, we divide our message into blocks, each of k bits, called datawords. We add r redundant bits to each block to make the length n = k + r. The resulting n-bit blocks are called codewords.
Error Detection Error Correction Hamming Distance
Minimum Hamming Distance
Topics discussed in this section:

## Slide 15
Datawords and codewords in block coding

## Slide 16
Process of error detection in block coding

## Slide 17
An error-detecting code can detect only the types of errors for which it is designed; other types of errors may remain undetected.
Note

## Slide 18
Structure of encoder and decoder in error correction

## Slide 19
The Hamming distance between two words is the number of differences between corresponding bits.
Note

## Slide 20
The minimum Hamming distance is the smallest Hamming distance between all possible pairs in a set of words.
Note

## Slide 21
CHECKSUM
The last error detection method discussed here is called the checksum. The checksum is used in the Internet by several protocols although not at the data link layer.
Idea One’s Complement Internet Checksum
Topics discussed in this section:

## Slide 22
Sender side checksum calculation:
The message is divided into 16-bit words.
The value of the checksum word is set to 0.
All words including the checksum are added using one’s complement addition.
The sum is complemented and becomes the checksum.
The checksum is sent with the data.

## Slide 23
Receiver side checksum calculation:
The message (including checksum) is divided into 16-bit words.
All words are added using one’s complement addition.
The sum is complemented and becomes the new checksum.
If the value of checksum is 0, the message is accepted; otherwise, it is rejected.

## Slide 24
Calculation of Checksum in the sender side and receiver side

## Slide 25
Example

## Slide 26: What kind of error is undetectable by the checksum?
The traditional checksum uses a small number of bits (16) to detect errors in a message of any size (sometimes thousands of bits). However, it is not as strong as the CRC in error-checking capability. For example, if the value of one word is incremented and the value of another word is decremented by the same amount, the two errors cannot be detected because the sum and checksum remain the same. Also if the values of several words are incremented but the total change is a multiple of 65535, the sum and the checksum does not change, which means the errors are not detected.

## Slide 27
Chapter 12
Multiple Access

## Slide 28
Data link layer divided into two functionality-oriented sublayers

## Slide 29
Summary of multiple-access protocols discussed in this chapter

## Slide 30
*RANDOM ACCESS
In random access or contention methods, no station is superior to another station and none is assigned the control over another. No station permits, or does not permit, another station to send. At each instance, a station that has data to send uses a procedure defined by the protocol to make a decision on whether or not to send.
ALOHA Carrier Sense Multiple Access
Carrier Sense Multiple Access with Collision Detection
Carrier Sense Multiple Access with Collision Avoidance
Topics discussed in this section:

## Slide 31
Frames in a pure ALOHA network

## Slide 32
Procedure for pure ALOHA protocol

## Slide 33
Vulnerable time for pure ALOHA protocol

## Slide 34
Frames in a slotted ALOHA network

## Slide 35
Behavior of three persistence methods

## Slide 36
Flow diagram for three persistence methods

## Slide 37
Collision of the first bit in CSMA/CD

## Slide 38
Collision and abortion in CSMA/CD

## Slide 39
Flow diagram for the CSMA/CD

## Slide 40
Energy level during transmission, idleness, or collision

## Slide 41
Timing in CSMA/CA

## Slide 42
In CSMA/CA, the IFS can also be used to define the priority of a station or a frame.

## Slide 43
In CSMA/CA, if the station finds the channel busy, it does not restart the timer of the contention window;
it stops the timer and restarts it when the channel becomes idle.

## Slide 44
Flow diagram for CSMA/CA

## Slide 45
*CONTROLLED ACCESS
In controlled access, the stations consult one another to find which station has the right to send. A station cannot send unless it has been authorized by other stations. We discuss three popular controlled-access methods.
Reservation Polling Token Passing

## Slide 46
Reservation access method

## Slide 47
Select and poll functions in polling access method

## Slide 48
Logical ring and physical topology in token-passing access method

## Slide 49
*CHANNELIZATION
Channelization is a multiple-access method in which the available bandwidth of a link is shared in time, frequency, or through code, between different stations. In this section, we discuss three channelization protocols.
Frequency-Division Multiple Access (FDMA) Time-Division Multiple Access (TDMA)
Code-Division Multiple Access (CDMA)

## Slide 50
Frequency-division multiple access (FDMA)

## Slide 51
In FDMA, the available bandwidth of the common channel is divided into bands that are separated by guard bands.

## Slide 52
Time-division multiple access (TDMA)

## Slide 53
In TDMA, the bandwidth is just one channel that is time shared between different stations.

## Slide 54
In CDMA, one channel carries all transmissions simultaneously.

## Slide 55
Chapter 14
Wireless LANs

## Slide 56
IEEE 802.11
IEEE has defined the specifications for a wireless LAN, called IEEE 802.11, which covers the physical and data link layers.
Architecture MAC Sublayer
Physical Layer
Topics discussed in this section:

## Slide 57
Figure 14.3 MAC layers in IEEE 802.11 standard

## Slide 58
Figure 14.4 CSMA/CA flowchart

## Slide 59
BLUETOOTH
Bluetooth is a wireless LAN technology designed to connect devices of different functions such as telephones, notebooks, computers, cameras, printers, coffee makers, and so on. A Bluetooth LAN is an ad hoc network, which means that the network is formed spontaneously.
Architecture Bluetooth Layers Baseband Layer
L2CAP

## Slide 60
Bluetooth layers

## Slide 61
Chapter 15
Connecting Devices
          Hubs
          Repeaters
          Bridges
          Switches
          Routers
          Gateway

## Slide 62
CONNECTING DEVICES
In this section, we divide connecting devices into five different categories based on the layer in which they operate in a network.
Passive Hubs
Active Hubs
Bridges
Two-Layer Switches
Routers
Three-Layer Switches
Gateways

## Slide 63
Five categories of connecting devices

## Slide 64
A repeater connecting two segments of a LAN
A repeater is a connecting device that operates in the physical layer of the Internet model. A repeater generates a signal, connects segments of a LAN, and has no filtering capability.

## Slide 65
A repeater connects segments of a LAN.
Note

## Slide 66
A repeater forwards every frame; it has no filtering capability.
Note

## Slide 67
A repeater is a regenerator, not an amplifier.
Note

## Slide 68
Function of a repeater

## Slide 69
A hierarchy of hubs

## Slide 70
A bridge has a table used in filtering decisions.
Note

## Slide 71
A bridge connecting two LANs

## Slide 72
A bridge does not change the physical (MAC) addresses in a frame.
Note

## Slide 73
UNIT 4

## Slide 74
Unit-4
Network Layer: & Transport Layer
Network Layer: Addressing IPV4 addresses - IPV6 Addresses Internet Protocol:IPv4 – IPv6Address mapping protocols: ARP – RARP Routing protocols: Unicast routing protocols: distance vector routing, Link State routing Multicast Routing protocols (Any two) Transport Layer: Process to process delivery – UDP – TCP Congestion control and QOS: Data traffic – congestion – congestion control – quality of service – techniques to improve quality of service.

## Slide 75
Unit-4 Teaching Hours: 10
Network Layer: & Transport Layer
Chapter 19 Network Layer Logical Addressing: IPv4 Addresses - IPV6 Addresses.
Chapter 20 Network Layer Internet Protocol: IPv4 – IPv6.
Chapter 21 Address Mapping Protocols: ARP – RARP.
Chapter 22 Routing protocols: UNICAST ROUTING PROTOCOLS: Distance vector routing, Link State routing. MULTICAST ROUTING PROTOCOLS (Any two).
Chapter 23 Transport Layer: Process to process delivery: UDP – TCP.
Chapter 24 Congestion control and Quality of Service (QoS): Data traffic – Congestion – Congestion control – Quality of service – Techniques to improve quality of service.

## Slide 76
76
ARP and RARP
Address Resolution Protocol and Reverse Address Resolution Protocol
Position of ARP and RARP in TCP/IP protocol suite
Notes: 76
76

## Slide 77
ARP and RARP
In dynamic mapping each time a machine knows one of the two addresses, it can use a protocol to find the other one.
Two protocols have been designed to perform dynamic mapping: Address resolution protocol(ARP) and Reverse address resolution protocol(RARP).
ARP maps a logical address to a physical address.
RARP maps a physical address to a logical address.
Notes: 77
77

## Slide 78
78
ARP
ARP associates an IP address with its physical address. On a typical physical network, such as a LAN, each device on a link is identified by a physical or station address that is usually imprinted on the NIC.
The topics discussed in this section include:
Packet Format
Encapsulation
Operation
ARP over ATM
Proxy ARP
Notes: 78
78

## Slide 79
79
ARP operation
Notes: 79
79

## Slide 80
Notes: 80
80

## Slide 81
*ARP packet
Notes: 81
81

## Slide 82
TCP/IP Protocol Suite
82
Notes: 82
82

## Slide 83
Four cases using ARP
Notes: 83
83

## Slide 84
84
An ARP request is broadcast; an ARP reply is unicast.
Note
Notes: 84
84

## Slide 85
85
Proxy ARP
A proxy ARP is an ARP that acts on behalf of a set of hosts.
Notes: 85
85

## Slide 86
TCP/IP Protocol Suite
86
RARP
RARP finds the logical address for a machine that only knows its physical address.
The topics discussed in this section include:
Packet Format
Encapsulation
RARP Server
Alternative Solutions to RARP
Notes: 86
86

## Slide 87
87
The RARP request packets are broadcast;
the RARP reply packets are unicast.
Note:

## Slide 88
TCP/IP Protocol Suite
88
RARP operation

## Slide 89
RARP packet

## Slide 90
Syllabus
UNICAST ROUTING PROTOCOLS:
Distance vector routing
Link State routing
MULTICAST ROUTING PROTOCOLS
Source-Based Tree Approach
Group-Shared Tree Approach
Chapter 22
Network Layer: Delivery, Forwarding, and Routing

## Slide 91
* UNICAST ROUTING PROTOCOLS
A routing table can be either static or dynamic. A static table is one with manual entries. A dynamic table is one that is updated automatically when there is a change somewhere in the Internet. A routing protocol is a combination of rules and procedures that lets routers in the Internet inform each other of changes.
* Intra- and Interdomain Routing
* Distance Vector Routing and RIP
* Link State Routing and OSPF
Path Vector Routing and BGP

## Slide 92
Popular routing protocols

## Slide 94
* Distance vector routing
Several routing algorithms, and the corresponding protocols, have been devised to find the best route among them; three have survived. In distance-vector routing, the first thing each node creates is its own least-cost tree with the rudimentary information it has about its immediate neighbours. The incomplete trees are exchanged between immediate neighbours to make the trees more and more complete and to represent the whole internet. In other words, in distance-vector routing, a router continuously tells all of its neighbours what it knows about the whole internet. The protocol that implements distance-vector routing is called Routing Information Protocol (RIP).

## Slide 95
* Link state routing
Another routing algorithm that has been used in the Internet is link-state routing. This method uses the term link-state to define the characteristic of a link (an edge) that represents a network in the internet. In this algorithm the cost associated with an edge defines the state of the link. In this algorithm, all routers flood the internet, with information related to their link states. When every router has the complete picture of the states, a link-state database can be created. The least-cost tree for each router and the corresponding forwarding table can be made from the link-state database. A protocol that implements link-state routing is called Open Shortest Path First (OSPF).

## Slide 96
Path-vector routing
Both link-state and distance-vector routing are based on the least-cost goal. However, there are instances where this goal is not the priority. Path-vector routing algorithms have been designed for this purpose. We can always insert policies in the forwarding table by preventing a packet from visiting a specific router. In path-vector routing, the best route from the source is the best path, the one that complies with the policy imposed. The protocol that implements path-vector routing is the Border Gateway Protocol (BGP).

## Slide 98
MULTICAST ROUTING PROTOCOLS
Multicasting
Multicast routing protocols.
Unicast, Multicast, and Broadcast Applications
Multicast Routing
Routing Protocols
Topics discussed in this section:

## Slide 99
Unicasting
In unicasting, the router forwards the received packet through only one of its interfaces.

## Slide 100
Multicasting
In multicasting, the router may forward the received packet through several of its interfaces.

## Slide 101
Multicasting versus multiple unicasting

## Slide 102
Taxonomy of common multicast protocols

## Slide 103
* Source-Based Tree Approach
In the source-based tree approach to multicasting, each router needs to create a separate tree for each source-group combination. In other words, if there are m groups and n sources in the internet, a router needs to create (m × n) routing trees. In each tree, the corresponding source is the root, the members of the group are the leaves, and the router itself is somewhere on the tree. We can compare the situation with unicast routing in which a router needs only one tree with itself as the root and all networks in the internet as the leaves. Although it may appear that each router needs to create and store a huge amount of information about all of these trees, there are two protocols that use this approach in the Internet today. These protocols use some strategies that alleviate the situation.

## Slide 104
* Group-Shared Tree Approach
In the group-shared tree approach, we designate a router to act as the core source for each group. The designated router, which is called the core router, acts as the representative for the group. Any source that has a packet to send to a member of that group sends it to the core center (unicast communication) and the core center is responsible for multicasting. The core center creates one single routing tree with itself as the root and any routers with active members in the group as the leaves. In this approach, there are m core routers (one for each group) and each core router has a routing tree, for the total of m trees. This means that the number of routing trees is reduced from (m × n) in the source-based tree approach to m in this approach. The reader may have noticed that we have divided a multicast delivery from the source to all group members into two deliveries. The first is a unicast delivery from the source to the core router; the second is the delivery from the core router to all group members. Note that the first part of the delivery needs to be done using tunneling. The multicast packet created by the source needs to be encapsulated in a unicast packet and sent to the core router. The core router decapsulates the unicast packet, extracts the multicast packet, and sends it to the group members. Although the reduction in number of trees in this approach looks very attractive, this approach has its own overhead: using an algorithm to select a router among all routers as the core router for a group.

## Slide 105
Chapter 23
Process-to-Process Delivery:
UDP and TCP

## Slide 106
PROCESS-TO-PROCESS DELIVERY
The transport layer is responsible for process-to-process delivery. The delivery of a packet, part of a message from one process to another. Two processes communicate in a client/server relationship.
Client/Server Paradigm Multiplexing and Demultiplexing
Connectionless Versus Connection-Oriented Service
Reliable Versus Unreliable
Three Protocols

## Slide 107
The transport layer is responsible for process-to-process delivery.
Note

## Slide 108
Types of data deliveries

## Slide 109
Port numbers

## Slide 110
IP addresses versus port numbers

## Slide 111
IANA ranges

## Slide 112
Socket address

## Slide 113
Multiplexing and demultiplexing

## Slide 114
Error control

## Slide 115
Position of UDP, TCP, and SCTP in TCP/IP suite

## Slide 116
USER DATAGRAM PROTOCOL (UDP)
The User Datagram Protocol (UDP) is called a connectionless, unreliable transport protocol. It does not add anything to the services of IP except to provide process-to-process communication instead of host-to-host communication.
Well-Known Ports for UDP User Datagram
Checksum
UDP Operation
Use of UDP

## Slide 117
*User datagram format

## Slide 118
UDP length = IP length – IP header’s length
Note

## Slide 119
Queues in UDP

## Slide 120
TCP
TCP is a connection-oriented protocol; it creates a virtual connection between two TCPs to send data. In addition, TCP uses flow and error control mechanisms at the transport level.
TCP Services TCP Features
Segment
A TCP Connection
Flow Control
Error Control

## Slide 121
Stream delivery

## Slide 122
Sending and receiving buffers

## Slide 123
TCP segments

## Slide 124
The bytes of data being transferred in each connection are numbered by TCP.
The numbering starts with a randomly generated number.

## Slide 125
The value in the sequence number field of a segment defines the
number of the first data byte contained in that segment.

## Slide 126
The value of the acknowledgment field in a segment defines the number of the next byte a party expects to receive.
The acknowledgment number is cumulative.

## Slide 127
*TCP segment format

## Slide 128
Control field

## Slide 129
Description of flags in the control field

## Slide 130
Connection establishment using three-way handshaking

## Slide 131
A SYN segment cannot carry data, but it consumes one sequence number.

## Slide 132
A SYN + ACK segment cannot carry data, but does consume one sequence number.

## Slide 133
An ACK segment, if carrying no data, consumes no sequence number.

## Slide 134
Data transfer

## Slide 135
Connection termination using three-way handshaking

## Slide 136
The FIN segment consumes one sequence number if it does not carry data.

## Slide 137
The FIN + ACK segment consumes one sequence number if it does not carry data.

## Slide 138
Sliding window

## Slide 139
A sliding window is used to make transmission more efficient as well as
to control the flow of data so that the destination does not become
overwhelmed with data. TCP sliding windows are byte-oriented.

## Slide 140
The receiver TCP delivers only ordered data to the process.

## Slide 141
UNIT 5 Syllabus
Chap 25 DNS: Name space, domain name space, distribution of name space.
Chap 26 Electronic-mail, Architecture, FILE transfer: FTP.
Chap 27 WWW and HTTP: Architecture web documents, HTTP.
Chap 30 Network Security: Introduction, definitions, two categories, symmetric key cryptography, traditional ciphers, asymmetric key cryptography.

## Slide 142
25.142
Chapter 25
Domain Name System
Topics discussed in this section:
Domain
Domain Name
Name-Address Resolution.
Root server.
Hierarchical name space.
Distribution of name space.
DNS in the Internet.
Flat name space.

## Slide 143
25.143
Domain Name System
The Domain Name System is client-server application that identifies each host on the Internet with a unique user-friendly name.
DNS organizes the name space in a hierarchical structure to decentralize the responsibilities involved in naming.

## Slide 144
25.144
Example of using the DNS service

## Slide 145
25.145
NAME SPACE
To be unambiguous, the names assigned to machines must be carefully selected from a namespace with complete control over the binding between the names and IP addresses.
Flat Name Space Hierarchical Name Space
Topics discussed in this section:

## Slide 146
25.146
DOMAIN NAME SPACE
To have a hierarchical name space, a domain name space was designed. In this design the names are defined in an inverted-tree structure with the root at the top. The tree can have only 128 levels: level 0 (root) to level 127.
Label
Domain Name: FQDN, PQDN.
Domain

## Slide 147
25.147
Domain name space

## Slide 148
25.148
Domain names and labels
Label: Each node in the tree has a label, which is a string with a maximum of 63 characters. Root label is null string. DNS requires that children of a node have different labels, which assures the uniqueness of the domain names. Domain Name: Each node in the tree has a domain name. A full domain name is a sequence of labels separated by dots (.). The domain names are always read from the node up to the root. The last label is the label of the root (null).

## Slide 149
25.149
FQDN (Fully Qualified Domain Name) : A FQDN is a domain name consisting of labels beginning with the host and going back through each level to the root name. or If a label is terminated by a null string, it is called a FQDN.
Eg. Challenger.atc.fhda.edu.
PQDN (Partially Qualified Domain Name):A PQDN is a domain name that does not include all the levels between the host and the root node or If a label is not terminated by a null string, it is called a PQDN. Eg. challenger

## Slide 150
25.150
Domain: A domain is a subtree of the domain space. The name of the domain is the domain name of the node at the top of the sub tree. A domain itself will be divided into domains (or subdomains as they are sometimes called).

## Slide 151
25.151
DISTRIBUTION OF NAME SPACE
The information contained in the domain name space must be stored. However, it is very inefficient and also unreliable to have just one computer store such a huge amount of information.
Hierarchy of Name Servers
Zone Root Server Primary and Secondary Servers
Topics discussed in this section:

## Slide 152
25.152
Hierarchy of name servers

## Slide 153
25.153
Zones and domains

## Slide 154
25.154
A primary server loads all information from the disk file; the secondary server
loads all information from the primary server.
When the secondary downloads
information from the primary, it is called zone transfer.

## Slide 155
25.155
Root Server
A root server is a server whose zone consists of the whole tree. A root server usually does not store any information about domains but delegates its authority to other servers, keeping references to those servers. There are several root servers, each covering the whole domain name space. The servers are distributed all around the world.

## Slide 156
25.156
DNS IN THE INTERNET
DNS is a protocol that can be used in different platforms. In the Internet, the domain name space (tree) is divided into three different sections:
Generic Domains
Country Domains
Inverse Domain

## Slide 157
25.157
DNS IN THE INTERNET

## Slide 158
25.158
Generic domains: These are according to their generic behavior. Each node in the tree defines a domain, which is an index to the domain name space database. Looking at the tree, we see that the first level in the generic domains section allows 14 possible labels. These labels describe the organization types.

## Slide 159
25.159
Generic domain labels

## Slide 160
25.160
Country domains
The country domains section uses two-character country abbreviations (e.g. The address anza.cup.ca.us can be translated to De Anza College in Cupertino, California, in the United States.)

## Slide 161
25.161
Inverse domain: The Inverse domain is used to map an address to a name. This may happen for e.g. when a server has received a request from a client to do a task. Although the server has a file that contains a list of authorized clients, only IP address of the client (extracted from the receiver IP packet) is listed. This type of query is called an inverse or pointer (PTR) query. To handle a pointer query, the inverse domain is added to the domain name space with the first-level node called arpa (for historical reasons). The second level is also one single node named in-addr (for inverse address). The rest of the domain refines IP address.

## Slide 162
25.162
RESOLUTION: Mapping a name to an address or an address to a name is called name-address resolution.
Resolver: DNS is a client-server application. A host that needs to map an address to a name or a name to an address calls a DNS client called a resolver.
Mapping Names to Addresses: Most of the time, the resolver gives a domain name to the server and asks for the corresponding address. In this case, the server checks the generic domains or the country domains to find the mapping.
Mapping Addresses to Names: A client can send an IP address to a server to be mapped to a domain name. This is called PTR. To answer queries of this kind, DNS uses the inverse domain. However, in the request, the IP address is reversed and the two labels in-addr and arpa are appended to create a domain acceptable by the inverse domain section.
Recursive Resolution, Iterative Resolution, Caching

## Slide 163
25.163
Recursive resolution: The client (resolver) can ask for a recursive answer from a name server. This means that the resolver expects the server to supply the final answer. If the server is the authority for the domain name, it checks its database and responds. If the server is not the authority, it sends the request to another server (the parent usually) and waits for the response. If the parent is the authority, it responds; otherwise, it sends the query to yet another server. When the query is finally resolved, the response travels back until it finally reaches the requesting client. This is called recursive resolution.

## Slide 164
25.164
Iterative resolution:In iterative resolution, the client may send its request to multiple servers before getting an answer.

## Slide 165
25.165
DNS MESSAGES
DNS has two types of messages: query and response. Both types have the same format.
The query message consists of a header and question records;
The response message consists of a header, question records, answer records, authoritative records, and additional records.

## Slide 166
25.166
TYPES OF RECORDS
Two types of records are used in DNS.
The question records are used in the question section of the query and response messages.
The resource records are used in the answer, authoritative, and additional information sections of the response message.
Question Record
Resource Record

## Slide 167
25.167
REGISTRARS
How are new domains added to DNS?
This is done through a registrar, a commercial entity accredited by ICANN (Internet Corporation for Assigned Names and Numbers). A registrar first verifies that the requested domain name is unique and then enters it into the DNS database. A fee is charged.

## Slide 168
25.168
DYNAMIC DOMAIN NAME SYSTEM (DDNS)
The DNS master file must be updated dynamically. The Dynamic Domain Name System (DDNS) therefore was devised to respond to this need. In DDNS, when a binding between a name and an address is determined, the information is sent, usually by DHCP to a primary DNS server. The primary server updates the zone. The secondary servers are notified either actively or passively.

## Slide 169
25.169
ENCAPSULATION
DNS can use either UDP or TCP.
In both cases the well-known port used by the server is port 53.
UDP is used when the size of the response message is less than 512 bytes because most UDP packages have a 512-byte packet size limit.
If the size of the response message is more than 512 bytes, a TCP connection is used.

## Slide 170
26.170
Chapter 26
Remote Logging
Electronic Mail,
File Transfer

## Slide 171
26.171
REMOTE LOGGING
It would be impossible to write a specific client/server program for each demand. The better solution is a general-purpose client/server program that lets a user access any application program on a remote computer.
TELNET

## Slide 172
26.172
TELNET is a general-purpose client/server application program.
Note

## Slide 173
26.173
Concept of NVT

## Slide 174
26.174
ELECTRONIC MAIL
One of the most popular Internet services is electronic mail (e-mail). Its architecture consists of several components that is discussed in this chapter:
Architecture User Agent
Message Transfer Agent: SMTP
Message Access Agent: POP and IMAP
Web-Based Mail

## Slide 175
26.175
First scenario in electronic mail

## Slide 176
26.176
When the sender and the receiver of an e-mail are on the same system,
we need only two user agents.
Note

## Slide 177
26.177
Second scenario in electronic mail

## Slide 178
26.178
When the sender and the receiver of an e-mail are on different systems, we
need two UAs and a pair of MTAs (client and server).
Note

## Slide 179
26.179
Third scenario in electronic mail

## Slide 180
26.180
When the sender is connected to the mail server via a LAN or a WAN,
we need two UAs and two pairs
of MTAs (client and server).
Note

## Slide 181
26.181
Fourth scenario in electronic mail

## Slide 182
26.182
Push versus pull in electronic email

## Slide 183
26.183
When both sender and receiver are connected to the mail server via a LAN or a WAN, we need two UAs, two pairs of MTAs
and a pair of MAAs.
This is the most common situation today.

## Slide 184
26.184
Services of user agent

## Slide 185
26.185
Some examples of command-driven user agents are mail, pine, and elm.
Note

## Slide 186
26.186
Some examples of GUI-based user agents are Eudora, Outlook, and Netscape.
Note

## Slide 187
26.187
Format of an e-mail

## Slide 188
26.188
E-mail address

## Slide 189
26.189
FILE TRANSFER
Transferring files from one computer to another is one of the most common tasks expected from a networking or internetworking environment.
As a matter of fact, the greatest volume of data exchange in the Internet today is due to file transfer.
File Transfer Protocol (FTP)

## Slide 190
26.190
FTP

## Slide 191
26.191
Using the control connection

## Slide 192
26.192
Using the data connection

## Slide 193
26.193
After the control connection is created, the FTP server sends the response.
The client sends its name.
The server responds.
The client sends the password.
The server responds (user log-in is OK).
The client sends the list command (ls reports) to find the list of files on the directory named report.
Now the server responds and opens the data connection.
The server then sends the list of the files or directories on the data connection.
The client sends a QUIT command.
The server responds.
FTP sample session:
The following shows an actual FTP session for retrieving a list of items in a directory.

## Slide 194
27.194
Chapter 27
WWW and HTTP
WWW and HTTP.
Architecture of WWW + URL + Browser.
Web documents & various categories of web documents.

## Slide 195
27.195
ARCHITECTURE
The WWW today is a distributed client/server service, in which a client using a browser can access a service using a server. However, the service provided is distributed over many locations called sites.
Client (Browser) Server Uniform Resource Locator
Cookies

## Slide 196
27.196
Architecture of WWW

## Slide 197
27.197
Browser

## Slide 198
27.198
URL

## Slide 199
27.199
*WEB DOCUMENTS
The documents in the WWW can be grouped into three broad categories: static, dynamic, and active. The category is based on the time at which the contents of the document are determined.
Static Documents
Dynamic Documents Active Documents
Topics discussed in this section:

## Slide 200
27.200
Static document

## Slide 201
27.201
Boldface tags

## Slide 202
27.202
Effect of boldface tags

## Slide 203
27.203
Beginning and ending tags

## Slide 204
27.204
Dynamic document using CGI

## Slide 205
27.205
Dynamic document using server-site script

## Slide 206
27.206
Dynamic documents are sometimes referred to as server-site dynamic documents.
Note

## Slide 207
27.207
Active document using Java applet

## Slide 208
27.208
Active document using client-site script

## Slide 209
27.209
Active documents are sometimes referred to as client-site dynamic documents.
Note

## Slide 210
27.210
*HTTP
The Hypertext Transfer Protocol (HTTP) is a protocol used mainly to access data on the World Wide Web. HTTP functions as a combination of FTP and SMTP.
HTTP Transaction Persistent Versus Nonpersistent Connection
Topics discussed in this section:

## Slide 211
27.211
HTTP transaction

## Slide 212
27.212
Request and response messages

## Slide 213
27.213
Request and status lines

## Slide 214
30.214
Chapter 30
Cryptography
In Greek “Secret Writing”
Definitions: Cryptography - Key in cryptography.
Types of cryptography.
*Symmetric-key cryptography & Example.
*Asymmetric-key cryptography & Example.
Mono alphabetic substitution with an example.
Differentiate between ciphertext and plain text.

## Slide 215
Cryptography is the science and art of transforming messages to make them secure and immune to attacks.
The plaintext is the original message before transformation; the ciphertext is the message after transformation.
An encryption algorithm transforms plaintext to ciphertext; a decryption algorithm transforms ciphertext to plaintext.
A combination of an encryption algorithm and a decryption algorithm is called a cipher.
The key is a number or a set of numbers on which the cipher operates.

## Slide 216
Definitions.
We can divide all ciphers into two broad categories:
Symmetric-key ciphers
Asymmetric-key ciphers.
In a symmetric-key cipher, the same key is used by both the sender and receiver. The key is called the secret key.
In an asymmetric-key cipher, a pair of keys is used. The sender uses the public key; the receiver uses the private key.

## Slide 217
Definitions.
A substitution cipher replaces one character with another character.
Substitution ciphers can be categorized into two broad categories:
  Monoalphabetic
  Polyalphabetic.

## Slide 218
30.218
Cryptography components

## Slide 219
30.219
Categories of cryptography

## Slide 220
Symmetric key cryptography.
In symmetric-key cryptography, the same key is used by both parties. The sender uses this key and an encryption algorithm to encrypt data; the receiver uses the same key and the corresponding decryption algorithm to decrypt the data.

## Slide 221
30.221
Symmetric-key cryptography

## Slide 222
30.222
In symmetric-key cryptography, the same key is used by the sender
(for encryption) and the receiver (for decryption).
The key is shared.

## Slide 223
Asymmetric key cryptography.
In asymmetric or public-key cryptography, there are two keys: a private key and a public key. The private key is kept by the receiver. The public key is announced to the public. In public-key encryption/decryption, the public key that is used for encryption is different from the private key that is used for decryption. The public key is available to the public; the private key is available only to an individual.

## Slide 224
30.224
Asymmetric-key cryptography

## Slide 225
Comparison: Let us compare symmetric-key and asymmetric-key cryptography.
Encryption can be thought of as electronic locking; decryption as electronic unlocking. The sender puts the message in a box and locks the box by using a key; the receiver unlocks the box with a key and takes out the message. The difference lies in the mechanism of the locking and unlocking and the type of keys used.
In symmetric-key cryptography, the same key locks and unlocks the box.
In asymmetric-key cryptography, one key locks the box, but another key is needed to unlock it.

## Slide 226
Substitution Cipher
A substitution cipher substitutes one symbol with another.
If the symbols in the plain-text are alphabetic characters, it can be replaced one character with another. If the symbols are digits,it can be replaced one digit with another.
Substitution ciphers can be categorized as either monoalphabetic or polyalphabetic ciphers.

## Slide 227
Mono alphabetic substitution.
In a monoalphabetic cipher, a character (or a symbol) in the plaintext is always changed to the same character (or symbol) in the ciphertext regardless of its position in the text. For example, if the algorithm says that character A in the plaintext is changed to character D, every character A is changed to character D. In other words, the relationship between characters in the plaintext and the ciphertext is a one-to-one relationship.

## Slide 228
30.228
Keys used in cryptography

## Slide 229
30.229
Comparison between two categories of cryptography

## Slide 230
30.230
SYMMETRIC-KEY CRYPTOGRAPHY
Symmetric-key cryptography started thousands of years ago when people needed to exchange secrets (for example, in a war). We still mainly use symmetric-key cryptography in our network security.
Traditional Ciphers Simple Modern Ciphers Modern Round Ciphers Mode of Operation

## Slide 231
30.231
Traditional ciphers

## Slide 232
30.232
A substitution cipher replaces one symbol with another.
Note

## Slide 233
30.233
The following shows a plaintext and its corresponding ciphertext. Is the cipher monoalphabetic?
Example 30.1
Solution
The cipher is probably monoalphabetic because both occurrences of L’s are encrypted as O’s.

## Slide 234
30.234
The following shows a plaintext and its corresponding ciphertext. Is the cipher monoalphabetic?
Example 30.2
Solution
The cipher is not monoalphabetic because each occurrence of L is encrypted by a different character. The first L is encrypted as N; the second as Z.

## Slide 235
30.235
The shift cipher is sometimes referred to as the Caesar cipher.
Note

## Slide 236
30.236
Use the shift cipher with key = 15 to encrypt the message “HELLO.”
Solution
We encrypt one character at a time. Each character is shifted 15 characters down. Letter H is encrypted to W. Letter E is encrypted to T. The first L is encrypted to A. The second L is also encrypted to A. And O is encrypted to D. The cipher text is WTAAD.
Example 30.3

## Slide 237
30.237
Use the shift cipher with key = 15 to decrypt the message “WTAAD.”
Solution
We decrypt one character at a time. Each character is shifted 15 characters up. Letter W is decrypted to H. Letter T is decrypted to E. The first A is decrypted to L. The second A is decrypted to L. And, finally, D is decrypted to O. The plaintext is HELLO.
Example 30.4

## Slide 238
30.238
A transposition cipher reorders (permutes) symbols in a block of symbols.
Note

## Slide 239
30.239
Transposition cipher

## Slide 240
30.240
ASYMMETRIC-KEY CRYPTOGRAPHY
An asymmetric-key (or public-key) cipher uses two keys: one private and one public. Two algorithms: RSA and Diffie-Hellman.
RSA (Ron Rivest, Adi Shamir and Leonard Adleman) Diffie-Hellman

## Slide 241: All the best……
Please remember this is only a small pointer to your topics. You need to read your text book.